receive
    Pattern1 [when Guard1] ->
        Expressions1;
    Pattern2 [when Guard2] ->
        Expressions2;
    ...
after
    Time ->
        ExpressionsTimeout
end

how does it work?
1. When we enter a receive statement, we start a timer (but only if an after section is present in the	expression).
2. Take the first message in the mailbox and try to match it against Pattern1, Pattern2 , and so on. If	the match succeeds, the message is removed from the mailbox, and the expressions	following the pattern are evaluated.
3. If none of the patterns in the receive statement matches the first message in the mailbox, then the	first message is removed from the mailbox and put into a “save queue.” The second message	in the mailbox is then tried. This procedure is repeated until a matching message is found or	until all the messages in the mailbox have been examined.
4. If none of the messages in the mailbox matches, then the process is suspended and will be	rescheduled for execution the next time a new message is put in the mailbox. When a new	message arrives, the messages in the save queue are not rematched; only the new message is	matched.
5. As soon as a message has been matched, then all messages that have been put into the save queue	are reentered into the mailbox in the order in which they arrived at the process. If a timer	was set, it is cleared.
6. If the timer elapses when we are waiting for a message, then evaluate the expressions	ExpressionsTimeout and put any saved messages back into the mailbox in the order in which	they arrived at the process.